## Slide 1
Eco-Loop
Autonomous Building Energy Optimization with AI Agents
Transforming buildings from passive energy consumers into self-correcting, carbon-aware autonomous systems
Student ID - 23BAI1584
Student Name – Aakarshak Swaraj
Problem Statement ID – 1A
Problem Statement Title- Eco-Loop Building Agents
PS Category- Software
Theme - Autonomous Building Energy Optimization with AI Agents

## Slide 2
Proposed Solution
THE PROBLEM
Buildings consume ~40% of global energy
Traditional BMS: rigid, rule-based schedules
No real-time adaptation to weather, occupancy, or grid signals
Significant energy waste
ECO-LOOP SOLUTION
AI-driven closed-loop HVAC optimization
Gemma 4 E2B LLM as cognitive engine
Physics-based simulation + intelligent decision-making
Model Context Protocol (MCP) for standardized integration
Multi-layer safety interlocks
KEY INNOVATION
Autonomy
Reasons about tradeoffs, not fixed rules.
Open source
Minimizes vendor lock-in.
Edge-ready
Runs on a single 8GB machine.

## Slide 3
Technical Approach
Technology Stack
Component
Technology
LLM Engine
Gemma 4 E2B (5.1B params)
LLM Runtime
Ollama (local inference)
Simulation
EnergyPlus + Python Surrogate
Agent Protocol
Model Context Protocol (MCP)
Backend
Python 3.11, LiteLLM, Pydantic
Dashboard
Streamlit + Plotly
Safety
4-Layer SafetyInterlock
Agent Decision Flow
Simulation Engine → Shared State (TelemetrySnapshot)
Shared State → EcoLoopAgent (context)
EcoLoopAgent → Gemma 4 E2B (System Prompt + Telemetry)
Gemma 4 E2B → EcoLoopAgent (JSON response)
EcoLoopAgent → Safety Interlock (validation)
Safety Interlock → HVAC System (validated command)
Real-time decision-making with physics-grounded safety ensures optimal, safe HVAC control.

## Slide 4
System Architecture
Eco-Loop AI Agent
Simulation, Gemma 4 E2B LLM, safety, shared state
External Signals
Grid tariffs, carbon, and weather inputs
Outputs
Dashboard and MCP server for insights
Building Environment
Sensors and HVAC system feeding data
The Eco-Loop system integrates real-time sensor data, weather forecasts, and grid signals to drive intelligent HVAC optimization through a closed-loop feedback mechanism.

## Slide 5
Feasibility and Viability
Feasibility Assessment
Criterion
Assessment
Hardware
Runs on 8GB RAM machine (consumer laptop tested)
LLM Size
Gemma 4 E2B = 5.1B params, Q4 quantized (~3GB)
Latency
5-15s per LLM call, 2-hour supervisory interval = negligible
Accuracy
Physics surrogate validated; EnergyPlus for production
Integration
MCP protocol = standard interface for any BMS
Challenges & Mitigations
LLM Hallucination
Pydantic validation + JSON parsing with retry
LLM Latency
Rule-based fallback + configurable timeout
Safety Risk
4-Layer Safety (Bounds | Deadband | Ramp-rate | Dwell)
Real Building Integration
MCP Protocol + BACnet/Modbus gateway

## Slide 6
Artifacts
Project Structure
honeywell_track1/
├── main.py (Orchestrator)
├── config/ (settings.yaml, baseline_medium_office.idf)
├── agent/ (controller.py, safety.py, prompts.py, schemas.py)
├── simulation/ (demo_engine.py, eplus_bridge.py, shared_state.py, comfort.py)
├── mcp_server/ (server.py)
└── dashboard/ (app.py)
Key Code Highlights
Agent Decision (controller.py)
response = completion(
model="ollama/gemma4:e2b",
messages=[...],
temperature=0.1,
max_tokens=256,
)
validated_args = HVACSetpointArgs.model_validate(parsed_json)
Safety Interlock (safety.py)
# Layer 1: Absolute bounds (18-28°C cool, 12-22°C heat)
# Layer 2: Minimum deadband (≥1.5°C between cool & heat)
# Layer 3: Ramp-rate limit (≤1.0°C/hour)
# Layer 4: Minimum dwell time (30 min between changes)
Physics Surrogate (demo_engine.py)
target = (cooling_sp + heating_sp) / 2.0
load = 0.08 * (outdoor_temp - zone_temp) + 0.03 * occupancy
zone_temp += 0.25 * (target - zone_temp) + load
Modular, production-ready codebase with comprehensive validation and safety mechanisms.

## Slide 7
Research and References
Core Technologies
Resource
Link
EnergyPlus (DOE)
https://energyplus.net/
Gemma 4 E2B (Google)
https://ai.google.dev/gemma
Ollama (Local LLM)
https://ollama.com/
Model Context Protocol
https://modelcontextprotocol.io/
LiteLLM
https://github.com/BerriAI/litellm
Streamlit
https://streamlit.io/
Research Papers & Standards
Topic
Reference
Building Energy Consumption
IEA Global Status Report 2024 — Buildings account for 40% of global energy
PMV Comfort Model
ISO 7730:2005 — Fanger's Predicted Mean Vote thermal comfort model
EnergyPlus Validation
DOE EnergyPlus Engineering Reference v24.2
LLM for Control
"Language Models as Controllers" — emerging research on LLM-driven process optimization
MCP Specification
Anthropic MCP Spec v1.0 — standardized agent-tool communication
ASHRAE 90.1
ASHRAE Standard 90.1-2022 — Energy Standard for Buildings
Demand Response
OpenADR 2.0 — Automated Demand Response standard
Traditional BMS = static rules → Eco-Loop = reasoning agent that weighs cost, carbon, and comfort in real-time using an open-source LLM, with physics-grounded safety guarantees.